## Slide 1
Lecture 3 Terminated Transmission Line
1. Voltage, Current and Input Impedance of A Terminated Line
2. Input Reflection Coefficient and Input Impedance
3. Matched Load, Short-circuit Load and Open-circuit Load
4. Quarter-wave Transformer
5. Voltage Standing Wave Ratio
6. Transmission Line with A Source and A Load
7. Reflected Power and Delivered Power
8. Code Example

## Slide 2
Terminating impedance (load)
Ampl. of voltage wave propagating in negative z direction at z = 0.
Ampl. of voltage wave propagating in positive z direction at z = 0.
1. Voltage, Current and Input Impedance of A Terminated Line

## Slide 3
Understanding the wave propagation

## Slide 4
What is V(-l )?
propagating forwards
propagating backwards
Voltage and current:
l  distance away from load
The current at z = - l is then
Terminating impedance (load)
from

## Slide 5
Total volt. at distance l from the load
Ampl. of volt. wave prop. towards load, at the load position (z = 0).
Similarly,
Ampl. of volt. wave prop. away from load, at the load position (z = 0).
L  Load reflection coefficient
l  Reflection coefficient at z = - l
Load reflection coefficient:

## Slide 6
Input impedance seen “looking” towards load at z = -l .
Input impedance:

## Slide 7
At the load (l = 0):
Reflection Coefficient

## Slide 8
At the load (l = 0):
Thus,
Recall

## Slide 9
Simplifying, we have
Hence, we have
sinh: 싸인에이취

## Slide 10
Impedance is periodic with period g/2
Note:
tan repeats when

## Slide 12
For the remainder of our transmission line discussion we will assume that the transmission line is lossless.

## Slide 13
2. Input Impedance and Input Reflection Coefficient

## Slide 14
Execise:
The reflection coefficient at the load is given by ΓL = 0.8 e j45°. The line is lossless and has characteristic impedance of 50 Ω.
1) Find the reflection coefficient at 0.2λg away from the load.
2) Find the input impedance at 0.2λg away from the load.
(Solution)

## Slide 15
Example: Reflectioin coefficient and input impedance of a terminated transmission line
Transmission line length L = 0.1 λg ; Load impedance ZL = 40 + j 70 Ω
Characteristic impedance Z0 = 50 Ω
1) Find the input reflection coefficient.
2) Fint the input impedance from the reflection coefficient.
3) Find the input impedance using ZL and L.
(Solution)

## Slide 16
Matched load: (ZL=Z0)
For any l
No reflection from the load
A
3. Matched Load, Short-circuit Load, and Open-circuit Load

## Slide 17
Short circuit load: (ZL = 0)
Always imaginary!
Note:
B
S.C. can become an O.C. with a g/4 trans. line
Short-circuit Load → Inductor

## Slide 18
Short-circuit Load

## Slide 19
Open-circuit Load → Capacitor

## Slide 20
Transmission Line Stub Equivalence

## Slide 21
Z0 from Short and Open Circuit Tests

## Slide 22
Example: Short-open test of a transmission line
f = 10 MHz, transmission line length L = 2 m
Open-circuit input impedance ZS = j 36 ; Short-circuit input impedance ZO = −j 69
Find Z0 and β, λg, εr the line.
(Answer)

## Slide 23
Using Transmission Lines to Synthesize Loads
A microwave filter constructed from microstrip.
This is very useful is microwave engineering.

## Slide 24
Exercise:
f = 300 MHz
Transmission line: length = 0.1 λg, Z0 = 50 Ω
1) Find the equivalent capacitance of an open-circuit transmission line.
2) Find the equivalent inductance of a short-circuit transmission line.
(Solution)

## Slide 25
4. Quarter-wave Transformer
so
Hence
This requires ZL to be real.
ZL
Z0
Z0T
Zin

## Slide 26
Exercise:
A load with impedance ZL = 20 Ω is connected to a quarter-wave transformer
with propagation constant β = 4π rad/m and characteristic impedance Z0 for
matching with a source impedance of 75 Ω. Find the length and characteristic
impedance of the quarter-wave transformer
(Solution)

## Slide 27
5. Voltage Standing Wave Ratio

## Slide 28
Exercise:
A load with impedance ZL = 20 −j 20 Ω is connected to a transmission line with
characteristic impedance Z0 = 50 Ω. Find the VSWR on the transmission line.
(Solution)

## Slide 29
6. Transmission Line with A Source and A Load

## Slide 30
Exercise:
A load with impedance ZL = 20 −j 20 Ω is connected to a transmission line whose
length is 0.2 wavelength and whose characteristic impedance Z0 is 50 Ω. The other
end of the transmission line is connected to a voltage source Vs = 10e j45° with
internal impedance Zs of 40+j60 Ω.
1) Find the voltage at the input of the transmission line.
2) Find the voltage at the load.
3) Find the power dissipated at the load.
(Solution)

## Slide 32
7. Reflected Power and Delivered Power

## Slide 33
Exercise:
A load with impedance ZL = 20 −j 20 Ω is connected to a transmission line with
characteristic impedance Z0 = 50 Ω. A voltage of 20e j45° is incident on the load.
1) Find the power Pi incident on the load.
2) Find the power Pr reflected from the load.
3) Find the power PL delivered to the load.
(Solution)

## Slide 34
8. Code Example

## Slide 35
# Microwave Engingineering, Lecture 2 Python Code
# Terminated transmission line: input reflection coefficient and input impedance
# Sample values:
# Input: RL=40, XL=40, L=0.1 wavelenth
# Output:
#
import cmath
import math
pi=3.14159265
while True:
RL=float(input('RL (ohm)='))
XL=float(input('XL (ohm)='))
Z0=float(input('Z0 (ohm)='))
L=float(input('L (wavelength)='))
j=complex(0.,1.)
ZL=complex(RL, XL)
GL=(ZL-Z0)/(ZL+Z0)
Gin=GL*cmath.exp(-j*2*2*pi*L)
Gin_mag, Gin_phase=cmath.polar(Gin)
Gin_dB=20*math.log(Gin_mag)
Zin=Z0*(1+Gin)/(1-Gin)
print('Input reflection coeffcient: mag, phase(deg)=',Gin_mag, Gin_phase)
print('Input reflection coefficint (dB)=',Gin_dB)
print('Zin=',Zin)

## Slide 36
'''
RL (ohm)=
20
XL (ohm)=
50
Z0 (ohm)=
50
L (wavelength)=
0.2
Input reflection coeffcient: mag, phase(deg)= 0.677834389404565 -1.022307778917341
Input reflection coefficint (dB)= -7.7770456858800845
Zin= (35.91076216402567-76.8526053239948j)
RL (ohm)=
'''